## Slide 1
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
CHALLENGE 04 · SMART MANUFACTURING
MachineSense
Affordable real-time machine health and energy monitoring
for SME manufacturers.
<10%
of commercial monitoring cost
Live
machine health + energy data
Explainable
AI, not a black-box alert
Vinit Shinde (Team Lead) Harsh Vyavahare Dipak Mane Shivam Sapkal
01 / 12

## Slide 2
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
The Problem -
SME factories run blind on energy and machine health
35–40%
of India's total energy is used by industry
₹15–25k+
cost of a commercial monitoring system
~900
large factories covered by India's PAT energy scheme — SMEs are not
The daily reality for SME manufacturers :
Machines fail without warning — the first sign of trouble is often a breakdown.
Energy waste goes unnoticed until the monthly electricity bill arrives.
No affordable way to know which machine, or which fault, is costing the most.
The "Industry 4.0" barrier: Smart manufacturing requires massive capital and IT infrastructure that SMEs don't have.
Skilled labor shortage: Relying on human intuition to "hear or feel" faults is subjective and unscalable.
Unplanned downtime: A single unexpected breakdown ruins production schedules and delivery deadlines.
Paper-based logging: Data is outdated by the time it reaches the manager's desk.
02 / 12

## Slide 3
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
Why Existing Approaches Fall Short
Commercial SCADA / monitoring
Priced for large industry (₹15,000–25,000+ per point). Out of reach for SMEs.
Government energy schemes (PAT)
Only covers ~900 large "Designated Consumers." The entire MSME segment sits outside it.
Manual inspection
Reactive, not predictive — a technician finds out after something has already gone wrong.
Basic IoT dashboards
Show raw numbers, but don't explain why an alert fired or what to actually do about it.
03 / 12

## Slide 4
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
Our Solution — MachineSense
A low-cost sensor node plus an explainable AI engine that tells a factory owner exactly what's wrong, what it's costing, and what to do next.
How it solves the problem
Retrofits any existing machine — no replacement, no PLC needed.
Costs under ₹2,500 per machine, versus ₹15,000–25,000+ commercially.
Now integrated with Schneider Electric PowerLogic™ meters for enterprise-grade reliability.
Now integrated with Schneider Electric PowerLogic™ meters for enterprise-grade reliability.
Catches mechanical wear and energy waste before the monthly bill or a breakdown reveals it.
Key differentiator
Every alert explains itself (which signal, how much) instead of an unexplained warning light — and the system is allowed to act on its own only for safe, reversible actions like switching on a cooling fan.
Sense
Understand
Explain
Act
04 / 12

## Slide 5
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
How MachineSense Works
End-to-end data flow, from the machine to the decision
Machine sensors
Current, voltage, vibration, temperature, RPM
Sensor node (ESP32 & Schneider Harmony Hub)
Sends readings over Wi-Fi / MQTT
Backend processing
Computes cost, runs anomaly detection
Database
Stores every reading and alert
Live updates
Pushed to the dashboard instantly
Dashboard
Status, explained alerts, cost, remaining-life estimate
05 / 12

## Slide 6
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
System Architecture & Tech Stack
ESP32 Sensors + Schneider PM5000 Modbus Meters
FastAPI backend (HTTP, MQTT + Modbus TCP ingestion)
Anomaly detection + power/cost service
PostgreSQL + WebSocket broadcast
React dashboard (multi-machine)
Tech stack
BACKEND FastAPI, Uvicorn, SQLAlchemy 2.0, Alembic, asyncpg
DATA PostgreSQL, MQTT (aiomqtt), WebSockets
ANALYTICS NumPy, SciPy — MAD-based anomaly detection
FRONTEND React 19, TypeScript, Vite, react-router
TESTING pytest, pytest-asyncio, httpx — 47 tests passing
06 / 12

## Slide 7
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
Machine Health & Energy Intelligence
Machine health
Vibration — Main signal for catching bearing wear early — ~50% of motor failures start here.
Temperature — Rising heat with no load change signals friction or overload.
Current + RPM — A machine drawing more current or running slower than baseline hints at mechanical resistance.
Detection method: median + MAD statistical baseline, with debounce logic so a single noisy reading never fires a false alert.
Energy intelligence
Live cost tracking — Real power, accumulated kWh, and ₹ cost — updated every few seconds.
SEC per good unit — Specific Energy Consumption (energy ÷ good units) — the real measure of efficiency, not raw kWh.
Day-to-day comparison — Explains output changes using idle time, slow-running periods, and health alerts — not just a number.
“Day 2 made 30% fewer good units than Day 1 despite equal run time — 42 minutes of unplanned stops, correlated with a vibration warning.”
07 / 12

## Slide 8
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
The AI Decision Engine
What makes this genuinely different from a sensor-plus-dashboard project
Baseline
Detect
Explain
Severity
Act
Inform
Shown on the dashboard only — all readings normal.
Alert
A person is notified; the decision to act stays human.
Automate
Safe, reversible action only — e.g. auto on/off a cooling fan when a machine overheats, saving energy, never touching the core machine itself.
Why it's novel: most hackathon monitoring projects stop at a red/green light. MachineSense explains every alert in plain language and is the only tier allowed to act — safely — on its own.
08 / 12

## Slide 9
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
Live Dashboard — Working Prototype
09 / 12

## Slide 10
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
Feasibility & Viability
Cost per machine
MachineSense Hybrid Node (ESP32 + Schneider)
₹1,800 – 2,500
Commercial monitoring system
₹15,000 – 25,000+
Open-source, free-to-use stack: FastAPI, React, PostgreSQL, MQTT — no licensing cost at any scale.
Scalability
● Already supports multiple machines, each with its own independent baseline.
● A fleet overview page lets one operator watch an entire factory at a glance.
● Roadmap: one sensor inferring many machines (NILM), and shared learning across whole factory clusters via federated learning — without any factory's raw data leaving its building.
10 / 12

## Slide 11
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
Impact & Benefits
8–12×
cheaper than commercial monitoring, per machine
Early
fault detection, days before failure — not after
Lower
unplanned downtime and energy waste
Who benefits
SME factory owners
Affordable visibility previously reserved for large industry.
Machine operators
Clear, explained alerts instead of unexplained red lights.
India's energy goals
A path for efficiency gains to reach the MSME segment PAT doesn't cover.
SDG alignment
SDG 7 — Affordable & Clean Energy
Cuts industrial energy waste at the source.
SDG 9 — Industry, Innovation & Infrastructure
Brings affordable smart-monitoring infrastructure to SMEs.
SDG 12 — Responsible Consumption
Reduces wasted energy and material per unit produced.
11 / 12

## Slide 12
YUVA YODHA
Energy Tech Hackathon 2026
SCHNEIDER ELECTRIC
What's Next
Remaining-useful-life
LSTM/Transformer models to predict days until service, not just Normal/Warning.
Federated learning
Factories improve one shared fault-detection model without ever sharing raw data.
On-device AI (TinyML)
Fault detection running on the sensor node itself — works even without internet.
Digital twin view
A live visual model of the machine, not just line charts.
Every sensor, every model, and every automated action exists to close the gap between “something changed” and “exactly why, and what to do about it.”
12 / 12